## Slide 1: COVID-19 Accessible Testing
Rapid Acceleration of Diagnostics (RADx®) Tech

## Slide 2: Presenters
RADx® Tech
  Brian Walsh, RADx Accessibility Program Manager, Deployment Core Team Lead
HomeLab
  Sarah Farmer, Director of Testing and Evaluation at the Center for Advanced Communications Policy at Georgia Tech, and the Managing Director of Georgia Tech’s HomeLab
Veranex Solutions
  Susan McDonald, Director Human Factors and User Research
  David Copeland, Director Human Centered Design
Notes: Sarah Farmer, Director of Testing and Evaluation at the Center for Advanced Communications Policy at Georgia Tech, and the Managing Director of Georgia Tech’s HomeLab
B.S. in psychology
Over 10 years of human factors experience
Her team has conducted over 85 evaluations during our work with RADx
Susan McDonald, Director Human Factors and User Research, Veranex Solutions
M.S. Engineering Management, Northeastern University
B.S. Human Factors Engineering, Tufts University
Human Factors and Ergonomics Society (HFES) member
AAMI Human Factors (HE) Committee member
Editor Human Factors in Healthcare Journal
David Copeland, Director Human Centered Design. Veranex Solutions
BFA Industrial Design, Carnegie Mellon University
Industrial Designers Society of America (IDSA) member

## Slide 3: RADx Tech Accessibility Program Agenda
Program Background
Accessible Tests Process
Status
Program Findings
Best Practices
RADx Tech Fast Track Accessible Tests Program
COVID-19 Home Test Experience Survey
Slide 3

## Slide 4: Program Inception
Jill Heemskerk, Deputy Director for the National Institute of Biomedical Imaging and Bioengineering (NIBIB):
"This was a big ah-ha moment for us, realizing that in our mad rush to make tests available as quickly as possible, we did not prioritize principles of universal design and accessibility, and we are very eager to correct this now. We held a listening session and formed a group that has stayed together with us in the subsequent months of designing and implementing the program that will be featured in this webinar."
Link to the full NIH press announcement pictured above
Slide 4

## Slide 5: Listening Session Led NIH & CIMIT
March 24, 2022
  Goals:
  Understand challenges to the accessibility of at-home tests,
  Discuss potential improvements, including their potential timescale
  Open lines of communication for ongoing discussion.
  Breakout groups addressed three focus areas:
  Individuals who are blind or low-vision
  Individuals with fine motor skill difficulties
  Older adults
Advocacy Attendees
Alliance on Aging and Vision Loss (AAVL)
American Council of the Blind (ACB)
American Foundation for the Blind (AFB)
American Geriatrics Society (AGS)
Independence Through Enhancement of Medicare Coalition (ITEM)
National Disability Rights Network (NDRN)
National Federation of the Blind (NFB)
World Institute on Disability (WID)
Slide 5

## Slide 6: Listening Session: Key Takeaways
There may not be a “one size fits all” solution for accessible COVID-19 tests
    Different solutions may be necessary to improve accessibility for different groups
Current design and medical equipment standards do not specify the accessibility standards that should be considered for at-home medical products
    An entirely new set of standards would need to clearly define the needs for different types of accessibility
This is an opportunity to inform future product accessibility standards
    COVID-19 tests are not the only at-home medical devices that need to be made more accessible to those with disabilities.
Slide 6

## Slide 7: RADx Tech Accessible Tests Program
A new program within RADx Tech
Targeted at OTC RADx tests
Required new, different resources and capabilities
Slide 7

## Slide 8: Advocacy & Government Partners Communications
Monthly Communications Meetings
  First meeting: May 11, 2022
  Purpose: Solicit input on accessibility challenges and solutions and provide updates on program progress
ADVOCACY GROUPS
American Council of the Blind
American Foundation for the Blind
National Federation of the Blind
Alliance on Aging and Vision Loss
American Geriatrics Society
National Disability Rights Network
World Institute on Disability
Independence Through Enhancement of Medicare and Medicaid Coalition
GOVERNMENT
Centers for Disease Control
Food and Drug Administration
National Council on Disability
National Eye Institute
National Center for Medical Rehabilitation Research
National Institute on Disability, Independent Living, and Rehabilitation Research/ Administration for Community Living
National Institute of Dental and Craniofacial Research
National Institute of Nursing Research
US Access Board
Slide 8

## Slide 9: RADx Tech OTC Test Program Process
Slide 9

## Slide 10: HomeLab
Slide 10

## Slide 11: Accessibility Analysis
Georgia Tech HomeLab
Seeks to understand the needs and desires of specific populations and to assist innovative companies in meeting their goals by providing a direct connection to laboratory and in-home testing resources.
Detailed qualitative & quantitative usability analysis of tests
Quantitative summary for each respective target population
Focus Groups
User Testing
Slide 11

## Slide 12: HomeLab Evaluation Process
Task Analysis
Identify the cognitive, physical, and sensory tasks associated with the procedure
Identify which tasks are essential to system success/failure
Determined if users were likely to be able to complete the task without assistance
Objective measurements
Force measurements (using a digital force gauge and a torque meter), font size, contrast ratios
Expert reviews
The test kit, protocol, and all instructional materials were evaluated. Researchers used the task analysis as scaffolding to walk through the testing protocol.
Slide 12

## Slide 13: HomeLab Accessibility Analysis
Report contents
Executive Summary
Methods
Results
  Pros
  Cons
Quantitative Task Analysis
  Users with no vision
  Users with low vision
  Users with limited dexterity
  Older adult users
Recommendations
Slide 13
Notes: https://www.nibib.nih.gov/covid-19/radx-tech-program/listening-session/agenda/executive-summary
We are in the process of adding additional resources especially in the aging population as that represents challenges in multiple accessibiity areas

## Slide 14: HomeLab Report – Sample Task Analysis
Example tasks include:
Open the outer box
Consume instructions
Remove seal from buffer tube
Open swab package
Dispense 3 drops of buffer into sample well on test device
Close tube cap
Interpret results
User Group | Number of inaccessible essential tasks | Number of inaccessible nonessential tasks
No vision | 18 | 2
Low vision | 5 | 1
Limited Dexterity | 2 | 0
Older Adults | 5 | 0
Slide 14

## Slide 15: Report Sample Excerpts
"Pros"
Features of the existing protocol, device, and instructions that enhance the user experience and should be preserved
"The tube is pre-filled with buffer liquid, which eliminates the need for any additional pouring or measuring steps"
"The device is large enough for most users to easily handle"
"The QR code present on the QRI directs users to the digital version of the QRI"
"Cons"
Features of the existing protocol, device, and instructions that could hinder the user experience
"The plastic pouches, with no texture or tear strip, may be difficult to open for users with reduced dexterity or strength."
"The foil seal on the buffer tube requires an excessive amount of force to open"
"The labeling on the test card is too small be read by many users."
"The digital QRI PDF document is not compatible with screen readers."
Slide 15

## Slide 16: HomeLab Report – Sample Recommendations
Reports for the Accessible Tests program included between 10 and 28 recommendations
The table below includes just a few examples
Issue number | Issue Description | Recommendations
4 | Users with reduced visual acuity or reduced contrast sensitivity may not be able to read the labelling on the outer box. | Ensure that all labelling is an accessible font size and contrast ratio
8 | The pouch containing the tube and other components may be difficult to open for users with reduced hand strength or dexterity | Implement texture and an easier to tear material for this packaging
9 | The dropper requires excess force to dispense sample and may be difficult for some users to squeeze | If liquid handling is required, ensure that no more than 5lb may be needed.
16 | There is no companion app, video, or user-friendly digital instructions to assist users who many have difficulty using paper instructions such as vision impaired users. | Include instructional materials in other modalities.
20 | Many of the images in the paper instructions are small in size and resolution, or low contrast. This may be challenging for users to interpret. [Provided examples omitted for identification reasons] | Use high contrast and high-quality images to depict all steps in the protocol.
Slide 16

## Slide 17: Subject Matter Experts
Slide 17

## Slide 18: Subject Matter Experts (SMEs)
Subject matter experts are critical to the success of the program
RADx Tech had to learn how to properly communicate & leverage their knowledge (accessible presentations, vernacular, etc.)
Currently 17 program SMEs supporting RADx:
  Trace Research & Development Center @ University of Maryland
  Non-visual Accessibility Analyst, National Federation of the Blind
  Designers from blind population
  Reviewers from aging population
  Reviewers from motor impairment population
Act in general consulting capacity for issues as they arise
Slide 18

## Slide 19: Subject Matter Expert Evaluation Process
Test kits provided to each SME
For consistency, SMEs used the HomeLab Task Analysis Template for reporting
Using the task analysis, SMEs indicated whether their user population(s) could successfully complete each task
Document issues, potential improvement and provide recommendations
Input is consolidated and provided to company & design firms

## Slide 20: Design & Implementation
Onboarded multiple design resources with accessibility experience
Differing areas of expertise: dexterity, visual, etc.
Integration of strategies encountered
Slide 20

## Slide 21: Veranex Solutions
Slide 21

## Slide 22
Concept to Commercial & Best in Class Expertise Under One Roof
Veranex has versatile cross-functional expertise dedicated to healthcare innovation
Slide 22
Notes: Discovery, Invention, & Definition
User needs discovery & opportunity definition
Requirements and rationale development
Human Centered concept generation
Product definition, design & engineering
Feasibility testing
Development & Verification
Verification and standards testing
Design Validation and usability engineering
Early feasibility through GLP studies
Manufactured in ISO registered and FDA inspected facilities
Preclinical GLP Studies
Regulatory Quality Systems, Clnical Serivces
  Regulatory, and quality systems consulting for first-of-kind to next-generation products
  Clinical operations, clinical strategy, site support and study design
Data Management Services
  Biostatistics
  Medical writing
  Data visualization
  Medical device safety services
  Statistical Management
  Market Access, Payer Landscape, Stakeholder Needs
  Global market pricing, reimbursement and market access strategy
  Precision Medicine
  Clinical and economic evidence development and communication
  Market Assessment and Business Strategy

## Slide 23
Scopes of Work
Heuristics and task analysis of 6+ testing kits with concept generation for
potential designs to improve accessibility.
Review and refine concepts then create prototypes of kit and app improvements.
Usability testing and evaluate findings of recommendations for kit improvements.
Slide 23

## Slide 24
Our Process
Slide 24

## Slide 25
Existing Test Kit Evaluations + Heuristics
Learnings: simulating low-vision and blind interaction with these products helped the project team empathize with the users and experience the accessibility issues first-hand. This was a starting point to compare Veranex findings to the provided concerns by the blind/low-vision SMEs.
Slide 25

## Slide 26
Concept Generation
Clear Problem Statement
Inspirational Imagery
Slide 26

## Slide 27
Concept Generation
Slide 27

## Slide 28
Down Selection + Concept Creation
Learnings:
Communicating concepts to low, or no vision users requires a complete shift in the way that we typically present ideas – to communicate verbally, versus visually
Slide 28

## Slide 29
SME Design Review
Clear problem statement regarding an accessibility issue with the kit
Our "recommendation" or suggested change to be presented to the kit vendor
Image description that verbally describes features of the concept drawings for blind SME’s
Simple line drawings to efficiently communicate the recommended change, particularly for low-vision
Concept drawings labelled with Alt Text for blind SME’s
Drawings converted to vector format and printed on emboss printers for SME evaluation
Learnings:
Accurately identifying the specific user group impacted by a particular problem is important. For instance, stating that a problem impacts the blind community when in reality it is a universal accessibility issue could make problematic assumptions about the capabilities of the blind community.
Slide 29

## Slide 30
SME Design Review
Learnings:
Accurately identifying the specific user group impacted by a particular problem is important. For instance, stating that a problem impacts the blind community when in reality it is a universal accessibility issue could make problematic assumptions about the capabilities of the blind community.
Slide 30

## Slide 31
Revisions and Vendor Review
After concepts were revised and down-selected using SME feedback, the updated concepts were presented to vendor companies
Learnings:
Vendors are limited by budget and manufacturing considerations. It's helpful to initially present concepts in their most basic yet aspirational form, but then also present some potential ways that the concept could be implemented considering the vendor's specific manufacturing limitations.
Slide 31

## Slide 32
Example – Adding a 'More Information' Feature to an App
Introducing a new “More Information” feature to an existing app to enhance usability with low vision and blind users.
Learnings:
Instead of treating blind and low-vision users as a separate user group and providing them with a distinct experience from users with full vision, it is better to design a universal design that everyone can access. This approach benefits not only blind and low-vision users, but also the rest. Although it takes more time and effort to create a universal design, it is ultimately a better approach.
Slide 32

## Slide 33
Next Steps – Physical Kit Improvements
What we're doing:
Prototype creation of down selected concepts to be used as stimuli in usability studies
In-depth interviews with target user groups to understand concept resonance
  Blind
  Low vision
  Aging (w/ dexterity challenges)
Three test tracks:​
  Universal concepts that are common across multiple kits​
  Concepts unique to RADx team members 1 and 2, both app-based and physical kit-based​
  Concepts (TBD) unique to RADx team members 3 and 4​
Slide 33

## Slide 34: RADx Tech Accessibility Status
Slide 34

## Slide 35: RADx Tech OTC Accessibility Test Funnel
24 RADx OTC Tests
  Traditional Lateral Flow Assay
  All-in-One Tests
  Reader assisted Lateral Flow Assays
  Reader assisted molecular tests
8 declined to participate/technical issues
4 on hold pending test technical development
12 active accessibility projects
Slide 35

## Slide 36: HomeLab Task Analysis
Of 13 products having completed analysis, the number of steps required ranges from 36-64 steps
On average 69% of essential tasks involved were not accessible
Test instructions generated the greatest number of accessibility issues.
On average 53% of recommendations were instructions-related.
Product | ​Analysis: Total Tasks​ | Analysis: Essential Tasks​ Not Accessible | ​Recommend: ​Instructions Related​
A | 36 | 100% | 78%​
B | 64 | 51% | 64%​
C | 38 | 62% | 81%​
D | 43 | 94% | 21%​
E | 43 | 59% | 40%​
F | 44 | 59% | 47%
G | 44 | 36% | 52%
H | 36 | 100% | 50%
I | 42 | 59% | 39%​
J | 45 | 73% | 50%
K | 42 | 80% | 43%
L | 42 | 52% | 58%
M | 41 | 71% | 61%​
Slide 36

## Slide 37: Key Design Consideration Examples
Low Vision
  High contrast between text and background
  14 point font or greater
  Thick, bold lines
No Vision
  Screen reader compatibility
  Components tactilely distinguishable from each other
  Results delivered in a non-visual manner
Dexterity
  No or very low pinch/grasp needed (strength & pain)
  Test can be conducted with one hand plus
  Test can be conducted with severe tremor and palsy (limit need for fine motor control)
Aging
  Simple, step-by-step instructions with additional context (e.g. video)
  Minimize memory demands
  Commonalities with low vision and dexterity
Slide 37

## Slide 38: Instructions
General framework and learnings applicable to all tests
Potentially fastest accessibility enhancement to existing tests
HomeLab & SME review provide feedback
  Small font size
  Lack of QR code/tactile code
  Inconsistent terminology
  Color and contrast issues
  Content placement
  Page layout to facilitate reading technology (flatbed scanner, camera)
  Should include text description of components to not rely on visuals
Creating mockups (physical & illustrative)
Target population reviews at Home Lab
Working in cooperation with FDA
Slide 38

## Slide 39: RADx Tech Accessibility Program Takeaways
Slide 39

## Slide 40: Key Takeaways
High level of enthusiasm
    Advocacy groups – moderated by historical experience
    Subject Matter Experts – recognize this as a unique opportunity to impact industry
    Companies – High engagement - “Ready Fire Aim” temptation
Real lack of accessibility information and process related to OTC Covid tests, IVDs & medical devices
    Extremely limited standards or guidance
    No codified process
    Real challenge for companies to get it right
Critical to actively engage target populations
    Continuous learning – all stakeholders
    Employ unique portfolio of tools, techniques, skills and tricks
    Insights related to daily living
Slide 40

## Slide 41: Key Takeaways
Problem Complexity
  Multiple stakeholders: NIH, FDA, companies, advocacy groups, users
  Advocacy groups helped us build an altogether new network of resources
  Home Lab provided systematic & structured process to assess & compare tests
  Not all interests and recommendations are completely aligned – best choices
Inherited Legacy Limitations
  Example: POC technologies migrating to OTC (counting of drops, "C" for control)
  Instructions for Use
  Walk the walk
      Monthly accessible advocacy meetings
      Design firm presentations had to be made accessible so SMEs could contribute
      Understand our limitations and biases – validation by experts
Slide 41

## Slide 42: RADx Best Practices
RADx Tech Accessibility goal to provide accessible COVID tests
Program has captured company-specific set of learnings that could perish when the program expires
Best Practices Initiative
    Objective: Capture and leverage learnings and experience from the RADx Tech Accessibility Program for current and future tests and medical devices
    Provide a roadmap for industry to build more accessible products from the inception
        Document learnings &amp; process
        Validation of design concepts
        Trial run of process and resources to ensure integrity
    Target Audience: commercial manufacturers and designers
Slide 42

## Slide 43: New Initiative – RADx Tech Fast Track Program
Additional initiative with accessibility emphasis
Application process was fully accessible
Review panel contains accessibility experts
    RADx Tech Fast Track Accessible Tests Program (approx. 50 applications)
      Accessibility specific focus for traditionally performing tests
      12-18 month timeline
    RADx Tech High Performance Tests Program (approx. 170 applications)
      Novel technologies that outperform current tests
      Accessibility included as a requirement
      3+ year timeline
Slide 43

## Slide 44: COVID-19 OTC Test Experience Survey
Slide 44

## Slide 45: User Survey
Advocacy Groups
Initiated at the strong urging of the advocacy groups
Advocacy membership offer real world feedback
Survey
Developed extensive survey based upon actual experiences with available tests
Analysis in each of the target populations: no/low vision, aging population, motor skills, combination
Hosted and managed by Home Lab
Approximately 550 respondents
Slide 45

## Slide 46: User Survey – User Population (%)
Segment | % Respon-dents
No Vision | 35%
No Vision/Older | 19%
Low Vision | 18%
Older Adult | 18%
Low Vision/Dexterity | 4%
Dexterity | 3%
No Vision/Dexterity | 2%
No Vision/Low Vision | 2%
Slide 46

## Slide 47: User Survey: How would you view purely digital instructions (no printed instructions)?
Slide 47

## Slide 48: User Survey: How would you view purely digital instructions (no printed instructions)?
Age Group | 18-24 | 25-34 | 35-44 | 45-54 | 55-64 | 65-74 | 75-84
Extremely Negatively | 0% | 0% | 14% | 11% | 18% | 12% | 23%
Somewhat Negatively | 9% | 9% | 11% | 9% | 22% | 24% | 14%
Neither Positively or Negatively | 28% | 28% | 19% | 23% | 24% | 23% | 18%
Somewhat Positively | 26% | 26% | 26% | 1% | 19% | 22% | 32%
Very Positively | 37% | 37% | 30% | 29% | 26% | 19% | 14%
Slide 48

## Slide 49: Thank You
Slide 49